Model Description

Tapiflex Essential 50 Tiles

The selected Tapiflex Essential 50 in tiles flooring belongs to the family of PVC vinyl flooring on 50 x 50 cm foam tiles.  The Stress Distributing Core (NRC) consists of a bonded recycled vinyl layer with a glass fiber felt. The unloaded top layer with class T abrasion resistance is reinforced by a photoreticulated polyurethane treatment with TopClean™ that permanently eliminates plating and provides a restorative spray.

The flooring contains more than 53% natural raw materials.

Its total weight is 3,270 g/m².

It is classified as Class 33 for commercial use and Class 42 for industrial use (EN 685).

It has a residual indentation of 0.15 mm (EN 433).

Its impact noise acoustic efficiency is 19 dB.

It has been treated with a Sanitized® bacteriostatic and fungistatic treatment.

Tapiflex Essential 50 Tiles

Specifications:

Classification (EN 685): commercial 33, industrial 42

Total thickness: 3.40 mm

Top layer thickness: 0.50 mm

Residual indentation (EN 433): 0.15 mm

Dimensional stability (EN 434): < 0.10%

Acoustic efficiency (ISO 140-8): ∆lw  19 dB

Flammability: Bfl - s1 on cement substrate

Abrasion group: T

Slipperiness (DIN 51130) R9

Light fastness (ISO 105-B02) ≥ 6

Environmental Data:

100% recyclable

Percentage of recycled materials: 28%

Natural raw materials: 53%

TVOC after 28 days: <100 µg/m3

ISO 14001 certified factory